PRODUCT DATASHEET

Product Model: Eclipse

Product Code: NTAG216-V1-NORMAL-B-BF-B

Updated: 10/01/2016

Approved by: John McLear

PHYSICAL CHARACTERISTICS
## Ring Dimensions
V = Varies on Ring Size
Black = Ring Blank
Gray = Inlay / Antenna
Sides / 10mm / 6.1mm / v / Radius 0.5mm / 8mm	Top / 8mm / 20mm / 6.1mm

### Front

2.3mm
v

v
## Available Sizes (United States Sizes)
4.5, 5, 6, 6.5, 7, 7.5, 8, 8.5, 9, 9.5, 10, 10.5, 11, 11.5, 12, 12.5, 13, 13.5, 14, 15, 16
## Fit style
Comfort Fit: Soft Radius
## Materials
Ring Blank: Hypoallergenic Hardened Advanced Ceramic
Inlay cover: Hypoallergenic Epoxy

## Colors
Blank: Black
Top Inlay: Black Fiber
Bottom Inlay: Black
Inlay FPCB: Black
## Engraving
“NFC Ring” on Bottom

## Antenna
2 of 20mm x 6mm Curved on FPCB (Flexible Printed Circuit Board)
Tin plated copper
NFC Ring Logo etched on FPCB (Not visible)

IC CHARACTERISTICS

Number of Ics(Integrated Components): 2
IC Manufacturer: NXP Semiconductors
IC Model: NTAG216
Full specifications: http://www.nxp.com/documents/data_sheet/NTAG213_215_216.pdf
Operating Frequency: 13.56Mhz
ISO/IEC: 14443A
User writable space: 888 bytes
Data retention: 10 years
Write endurance: 100,000
IC Type: Sawn Wafer
IC Mount Type: Wire bonded w/ glue

## Security
Manufacturer programmed 7-byte UID for each device
Pre-programmed Capability container with one time programmable bits
Field programmable read-only locking function
ECC based originality signature
32-bit password protection to prevent unauthorized memory operations

OPERATING LIMITATIONS
## Forces
Can withstand drops onto most surfaces from 5M. Drops onto Ceramic and harder surfaces should be avoided.

## Temperatures
Overall recommended temperature maximum exposures:
Min: -20c
Max: 110c

IC Limitation:
Min: -55c
Max: 125c

Epoxy Limitation:
Min: -20c
Max: 110c

Blank Limitation:
Min: -85c
Max: 1668c

## Water resistance
IP66
Protected from Total dust ingress
Protected from high pressure washer jets from any direction

PATENTS AND LEGAL
## Patents:

US 2015/0042450-A1: Covers:

Inserting NFC inlays in a Ring Embodiment (Both metallic and ceramic)
Using Hand Gestures to perform different tasks with a Ring including unlocking a phone and	sharing contact information
Interacting between a Ring and an access control system
Current Licensees:
Visa Collab Inc
Mastercard Inc
DangerousThings Inc

## Trademarks:

“NFC Ring” is a registered Trademark of McLear Ltd

BEHAVIORAL CHARACTERISTICS

## Operating Range

Keyduino Nano: 30mm
Elechouse PN532: 25mm
Samsung SHS-1321: 15mm
Nexus 5: 15mm
ACR122: 20mm
HTC One M8: 5mm