PRODUCT DATASHEET

Product Model: Alpha Signature

Product Code: NTAG203-V1-ALPHA-T-B-T

Updated: 10/01/2016

Approved by: John McLear

PHYSICAL CHARACTERISTICS
## Ring Dimensions
V = Varies on Ring Size
Black = Ring Blank
Gray = Inlay / Antenna
Sides / 10mm / 10.1mm / v / Radius 0.5mm / 13mm	Top / 13mm / 20mm / 10.1mm

### Front

2mm
v

v
## Available Sizes (United States Sizes)
4.5, 5, 5.5, 6, 6.5, 7, 7.5, 8, 8.5, 9, 9.5, 10, 10.5, 11, 11.5, 12, 12.5, 13, 13.5, 14, 14.5, 15, 15.5, 16
## Fit style
Comfort Fit: Soft Radius
## Materials
Ring Blank: Hypoallergenic Titanium
Inlay cover: Hypoallergenic Epoxy

## Colors
Blank: Silver Titanium
Top Inlay: Black
Bottom Inlay: Transparent
Inlay FPCB: Gold Yellow
## Engraving
None

## Antenna
2 of 20mm x 10mm Curved on FPCB (Flexible Printed Circuit Board)
Tin plated copper
NFC Ring Logo etched on FPCB

IC CHARACTERISTICS

Number of Ics(Integrated Components): 2
IC Manufacturer: NXP Semiconductors
IC Model: NTAG203
Full specifications: http://www.nxp.com/documents/short_data_sheet/NTAG203_SDS.pdf
Operating Frequency: 13.56Mhz
ISO/IEC: 14443A
User writable space: 144 bytes
Data retention: 5 years
Write endurance: 10,000
IC Type: Sawn Wafer
IC Mount Type: Wire bonded w/ glue

## Security
Anti-cloning support by unique 7-byte serial number for each device.
32-bit user programmable OTP(One Time Programmable) area.
Field programmable read-only locking function per page for first 512 bits.
Read-only locking per block for rest of memory.

OPERATING LIMITATIONS
## Forces
Can withstand drops onto all surfaces from 5M

## Temperatures
Overall recommended temperature maximum exposures:
Min: -20c
Max: 110c

IC Limitation:
Min: -55c
Max: 70c (note that the IC is protected by Epoxy and a heat resistant glue)

Epoxy Limitation:
Min: -20c
Max: 110c

Blank Limitation:
Min: -85c
Max: 1668c

## Water resistance
IP66
Protected from Total dust ingress
Protected from high pressure washer jets from any direction

PATENTS AND LEGAL
## Patents:

US 2015/0042450-A1: Covers:

Inserting NFC inlays in a Ring Embodiment (Both metallic and ceramic)
Using Hand Gestures to perform different tasks with a Ring including unlocking a phone and	sharing contact information
Interacting between a Ring and an access control system
Current Licensees:
Visa Collab Inc
Mastercard Inc
DangerousThings Inc

## Trademarks:

“NFC Ring” is a registered Trademark of McLear Ltd

BEHAVIORAL CHARACTERISTICS

## Operating Range

Keyduino Nano: 4mm
Elechouse PN532: 3mm
Samsung SHS-1321: 2mm
Nexus 5: 2mm
ACR122: 1mm
HTC One M8: 1mm